## Slide 1
GNSS Front End
From satellite RF to acquisition-ready samples
GNSS RECEIVERS | MASTER’S LECTURE | NCGSA–IST
RF →
Notes: Open the live dashboard at https://nvgl.ncgsa.org.pk/front-end/. The lecture follows its nine lessons. The receiver values are an illustrative GPS L1 front-end example.

## Slide 2
LECTURE MAP
Nine dashboard lessons. One receive chain.
Each lesson answers a practical receiver-design question.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
02
01
Complete chain
From antenna to samples
02
GNSS antenna
RHCP, gain, phase centre
03
Noise & sensitivity
Why signals appear buried
04
Filtering
Keep the useful spectrum
05
Mixing
RF to intermediate frequency
06
Sampling
Avoid unwanted alias overlap
07
ADC & AGC
Quantize without clipping
08
Sample inspection
Waveform · histogram · PSD
09
Acquisition handoff
Digital IF and sample metadata
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 3
RECEIVER PERSPECTIVE
What the front end actually does
It conditions a very weak analog signal and represents it as digital samples.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
03
SATELLITE SIGNAL
L-band RF at the receiving antenna
FRONT END
Select · amplify · translate · sample
BASEBAND DSP
Acquire PRN / estimate Doppler / track
The front end does not “find satellites” yet; it prepares faithful samples for the algorithms that do.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 4
LESSON 01 · COMPLETE FRONT END
Follow the signal — and the clock
Dashboard reference architecture: GPS L1, real intermediate-frequency sampling.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
04
ANTENNA
RHCP
CABLE
loss
RF FILTER
select
LNA
low NF
MIXER
downconvert
IF FILTER
band limit
ADC
digitize
10 MHz reference → frequency synthesizer → LO + sampling clock
Challenge: name the first stage that should reject strong out-of-band interferers.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 5
LESSON 01 · FREQUENCY PLAN
A worked GPS L1 front-end frequency plan
Read these values directly in the dashboard and verify the arithmetic.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
05
1575.420
RF carrier (MHz)
1527.680
Local oscillator (MHz)
47.740
Analog IF (MHz)
38.192
Sample rate (MS/s)
fIF = | fRF − fLO | = |1575.420 − 1527.680| = 47.740 MHz
Shared reference clock: 1,527.68 MHz ÷ 40 = 38.192 MHz sampling clock.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 6
LESSON 02 · GNSS ANTENNA
Antenna: convert the arriving wave into RF voltage
A GNSS antenna is part of the measurement system, not merely a connector.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
06
Polarization
GNSS downlinks are normally RHCP. Matching the sense of rotation limits mismatch loss.
Gain & pattern
Look at sky coverage, elevation response and unwanted low-angle reception.
Phase center
PCO and PCV calibration matter in precise carrier-phase measurements.
Dashboard controls: change axial ratio to see how polarization mismatch reduces received power.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 7
LESSON 02 · POLARIZATION
Axial ratio puts a number on circularity
Lower axial ratio is closer to ideal circular polarization.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
07
0 dB
Ideal circular polarization
3 dB
Major/minor amplitude ≈ 1.41 : 1
20 dB
Highly elliptical / nearly linear
AR(dB) = 20 log₁₀ (Emajor / Eminor)
In the dashboard’s ideal same-handed circular-wave example, AR = 3 dB adds ≈ 0.125 dB loss.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 8
LESSON 02 · RECEIVED POWER
An illustrative GPS L1 link budget
Long range and free-space spreading explain why receiver signals are so weak.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
08
27 W
Transmit power
13 dBi
Transmit antenna gain
20,200 km
Slant range
0 dBi
Receive antenna gain
Received L1 power ≈ −157.69 dBW = −127.69 dBm
Use the dashboard to inspect wavelength (≈ 0.1903 m) and effective area.
The link budget is a teaching example; measured C/N₀ also depends on the antenna, environment and receiver.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 9
LESSON 03 · WEAK SIGNALS
Why GPS signals look like noise before correlation
Wideband thermal noise can dwarf instantaneous signal power.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
09
THERMAL NOISE FLOOR
N = k T B
Temperature × bandwidth sets admitted noise.
290 K
Reference temperature
2 MHz
Example noise bandwidth
At B = 2 MHz and 290 K, thermal noise is about −110.96 dBm.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 10
LESSON 03 · NOISE METRICS
C/N₀ and SNR are different measurements
C/N₀ uses noise spectral density; SNR depends on chosen bandwidth.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
10
C/N₀
Carrier-to-noise-density ratio, reported in dB-Hz. A common receiver signal-quality metric.
SNR in bandwidth B
SNR(dB) = C/N₀(dB-Hz) − 10log₁₀ B(Hz)
Example: C/N₀ ≈ 43.98 dB-Hz → SNR ≈ −19.04 dB in 2 MHz.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 11
LESSON 03 · SENSITIVITY
Place low-noise gain before avoidable losses
The Friis noise-factor cascade weights later noise by preceding gain.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
11
Ftotal = F₁ + (F₂−1)/G₁ + (F₃−1)/(G₁G₂) + …
Better chain
ANTENNA → LNA → LOSSY CABLE
Worse chain
ANTENNA → LOSSY CABLE → LNA
Dashboard experiment: compare an 8 dB cable loss before versus after a 30 dB, 2.5 dB-NF LNA.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 12
LESSON 04 · SELECT THE BAND
Three filters. Three jobs.
Preselection, IF selectivity and final band-limit each protect a different stage.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
12
RF preselection
50 MHz
Suppress distant RF blockers
IF selection
18 MHz
Reject mixer products / image residue
Final band limit
6 MHz
Constrain the band presented to ADC
Selectivity is useful only if the filter does not remove the signal information we need.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 13
LESSON 04 · BANDWIDTH TRADE-OFF
Narrow filters reduce noise — but can distort code
A lower noise bandwidth is not automatically a better navigation signal.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
13
GPS C/A main-lobe spectral nulls: ±1.023 MHz around L1
≈ 2.046 MHz main-lobe width
Use dashboard widths of 1, 2.046, 6 and 12 MHz; observe SNR and signal-fidelity trade-offs.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 14
LESSON 05 · TRANSLATE THE CARRIER
Mixing moves a band without removing its modulation
Multiplication produces a difference and a sum frequency.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
14
cos A · cos B = ½ cos(A − B) + ½ cos(A + B)
1575.42 MHz
GPS L1 RF
47.74 MHz
Difference IF — retain
3103.10 MHz
Sum — reject with filter
Local oscillator fLO = 1527.68 MHz. The navigation code and Doppler move with the carrier.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 15
LESSON 05 · IMAGE-FREQUENCY PROBLEM
The mixer cannot tell which side of LO produced IF
Two input frequencies can map to the same output difference.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
15
IMAGE RF
1479.94 MHz
LOCAL OSCILLATOR
1527.68 MHz
WANTED GPS L1
1575.42 MHz
|1479.94 − 1527.68| = |1575.42 − 1527.68| = 47.74
RF preselection rejects image-band energy before the mixer has made it indistinguishable.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 16
LESSON 06 · SAMPLING
Sampling is a clocked measurement of the IF waveform
The sampling frequency governs spacing in time and the digital frequency map.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
16
Sample instants tₙ = n / fₛ | Time step Tₛ = 1 / fₛ
For fₛ = 38.192 MS/s, each sample is separated by ≈ 26.18 ns.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 17
LESSON 06 · BANDPASS SAMPLING
A higher analog IF can fold to a lower digital IF
This works only when the entire occupied band folds without overlapping copies.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
17
44.74–50.74
Analog passband (MHz)
38.192
Sampling clock (MS/s)
6.548–12.548
Digital band (MHz)
fIF,digital = 47.740 − 38.192 = 9.548 MHz
Digital Nyquist limit = fₛ/2 = 19.096 MHz; the 6 MHz band remains inside 0–19.096 MHz.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 18
LESSON 06 · DASHBOARD EXPERIMENT
Choosing fₛ is a band-overlap problem
The IF centre alone is not enough: test both edges of the occupied spectrum.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
18
38.192 MS/s
Valid
Example design
28 MS/s
Valid*
Inverted spectral ordering
30 MS/s
Problem
Band crosses a folding boundary
47.74 MS/s
Problem
IF folds across zero
*A spectrally inverted alias can still be handled digitally if the receiver models the inversion.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 19
LESSON 07 · ADC
The ADC discretizes time and amplitude
Quantization is an explicit trade-off between sample precision and data rate.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
19
1 bit
2 levels
2 bits
4 levels
4 bits
16 levels
8 bits
256 levels
L = 2ᵇ amplitude levels Δ = Vspan / 2ᵇ
For a normalized −1 to +1 V range: 4 bits → 16 levels → 0.125 V step.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 20
LESSON 07 · GAIN CONTROL
Set gain high enough to use ADC codes — not to clip
Automatic gain control keeps noise and interference inside converter range.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
20
Too little gain
Samples crowd around the central codes; dynamic range is poorly used.
Useful gain
The histogram spans a healthy portion of available levels.
Excessive gain
Input excursions hit the upper and lower rails; clipping distorts spectrum.
Dashboard: change bits (1 / 2 / 4 / 8) and RMS/full-scale; watch clipping and level occupancy.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 21
LESSON 08 · SAMPLE INSPECTION
Three plots reveal different faults
No single plot can verify that a particular GNSS satellite has been acquired.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
21
TIME WAVEFORM
Clipping and transients
HISTOGRAM
Code occupancy and symmetry
SPECTRUM / PSD
Band location, noise, interferers
A shaped noise spectrum is not proof of code correlation or satellite identity.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 22
LESSON 09 · HANDOFF
Digital samples are meaningful only with metadata
Acquisition needs the samples, clock rate, centre frequency and format.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
22
38.192 MS/s
Sample rate
9.548 MHz
Digital IF
Real-valued
Sample representation
4 bits
ADC resolution
1 ms of GPS C/A contains 38,192 digital samples and 1,023 chips.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 23
AFTER THE FRONT END
Acquisition searches code delay and Doppler
A sampled IF waveform becomes an input to local-code and carrier hypotheses.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
23
DIGITAL IF
x[n], fₛ, fIF and sample format
WIPE-OFF + CORRELATE
Local carrier and PRN replicas
ACQUISITION RESULT
Code phase, Doppler and metric
xD[n] = r[n] · exp{−j2π(fIF,digital + fD) n / fₛ}
The Front End dashboard demonstrates preparation; its output is not automatically transferred to Acquisition.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 24
DASHBOARD LAB · PART A
Diagnose the analog signal chain
Work sequentially through lessons 01–05 and record a brief engineering justification.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
24
01
Trace eight analog/digital blocks and both LO/clock branches.
02
Sweep axial ratio: 0, 3, 6 and 20 dB. Note mismatch trend.
03
Move 8 dB cable loss before/after LNA. Compare NF.
04
Compare filter bandwidths: 1, 2.046, 6 and 12 MHz.
05
Compute difference, sum and image frequency for GPS L1.
Record: control setting → observation → physical explanation.
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 25
DASHBOARD LAB · PART B
Verify the digital conversion and handoff
Work through lessons 06–09. Present the observations, not just screenshots.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
25
06
Test fₛ = 38.192, 28, 30 and 47.74 MS/s. Explain aliases.
07
Compare 1, 2, 4 and 8-bit output; monitor clipping.
08
Read waveform, histogram and PSD; identify one fault per view.
09
List handoff metadata and compute samples in 1 ms.
Dashboard URL: https://nvgl.ncgsa.org.pk/front-end/
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 26
LEARNING CHECK
Can you defend the front-end design?
Discuss before switching to the acquisition dashboard.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
26
01
Why does pre-LNA cable loss hurt sensitivity?
02
How can two different RF inputs yield the same IF?
03
Why check aliasing of band edges, not only centre?
04
What does a histogram reveal that a PSD cannot?
05
What metadata is essential for local-carrier wipe-off?
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).

## Slide 27
TAKE-HOME SYNTHESIS
From a weak RF wave to useful digital evidence
A receiver succeeds when analog fidelity and digital assumptions agree.
GNSS FRONT END | NCGSA VIRTUAL GNSS LABORATORY
27
PRESERVE
Signal power, phase and wanted bandwidth
TRANSLATE
Use filtering, mixing and timing coherently
REPRESENT
Sample and quantize without ambiguity
Next: PRN acquisition → carrier/code tracking → navigation solution
Notes: Dashboard: https://nvgl.ncgsa.org.pk/front-end/
Illustrative values and receiver architecture follow the NCGSA Virtual GNSS Laboratory Front End lessons. GNSS front-end hardware varies by receiver design.
Suggested reading on dashboard: GNSS_Front_End.pdf and GPS_Front_End_Lecture.pdf. This lecture is structured on the dashboard and is not a specification of a particular physical receiver.
Source: NCGSA Virtual GNSS Laboratory — GNSS Front End (https://nvgl.ncgsa.org.pk/front-end/).